## Slide 1: How to Control Unity Objects from Arduino

## Slide 2: Before you Start…
Ensure you have followed the steps in the Setup Guide
  Unity installed
  Ardity package installed & set up
  Arduino IDE installed & set up

## Slide 3: Creating an Object
Right click on the Hierarchy area on the left
Create a new Cube 3D object
  3D Object > Cube

## Slide 4: Adding Code to the Cube
Go to Assets > Ardity > Scripts
Click on the Cube object
Drag “SerialController.cs” into the Cube inspector area
Drag the code file into the space on the right

## Slide 5: Adding Code to the Cube
Download “MyListener.cs” & move it to Assets
Click on the Cube object
Drag “MyListener.cs” into the Cube inspector area
Drag the code file into the space on the right

## Slide 6: Arduino Code
Download & open Sketch dec8a.ino
Upload the code into your Arduino
Ensure you go to Tools and select the correct port and board type

## Slide 7: Arduino Circuit Setup
Notes: https://docs.arduino.cc/built-in-examples/basics/DigitalReadSerial

## Slide 8: More about the Arduino Code…
Setup
  Begins serial clock at 9600 Baud Rate
  Sets pin 2 to input mode
Loop
  Reads the signal from the button (on or off)
  Sends the signal into the serial port
  Waits for 1 second

## Slide 9: More about the C# Code…
MyListener.cs
Initialise cube modifier as game object
Sets speed variable to the message received from Arduino times 10
Moves cube to the right