## Slide 1: How to Control Arduino LED from Unity

## Slide 2: Before you Start…
Ensure you have followed the steps in the Setup Guide
  Unity installed
  Ardity package installed & set up
  Arduino IDE installed & set up

## Slide 3: Creating an Object
Right click on the Hierarchy area on the left
Create a new Cube 3D object
  3D Object > Cube

## Slide 4: Adding Code to the Cube
Download “LEDClick.cs”
Add into your project Assets Folder
Click on the Cube object
Drag the code file into the space on the right

## Slide 5: Arduino Code
Download & open Sketch dec9a.ino
Upload the code into your Arduino
Ensure you go to Tools and select the correct port and board type

## Slide 6: Arduino Circuit Setup
Plug the longer end of the LED into Pin 13
Plug the shorter end into GND (Ground)
Notes: http://www.learningaboutelectronics.com/images/Arduino-LED-flasher.png

## Slide 7: More about the Arduino Code…
Setup
  Sets pin 13 to output mode
  Begins serial clock at 9600 Baud Rate
Loop
  If the serial port is open, read the data from the port
  If the value received is “1”, sets variable “ledState to 1”
  Else, ledState remains as 0
  Writes the value of ledState to Pin 13
  This will turn the LED on or off accordingly
  Wait for 50 milliseconds

## Slide 8: More about the C# Code…
Declaration of Cube object and Serial Port object set to port 13 at 9600 Baud rate (same as Arduino)
Start
  Opens serial port (set serial port according to your computer)
Update
  If a left click input is detected:
  Check if variable LED state is at 1 or 0
  If the LED is off, writes “1” to serial port (recall that the Arduino code checks for this “1”, and changes LEDState to 0
  The purpose of LEDState: the next time we left click, we want the LED to turn off. Hence the variable stores the next intended action for the LED
  Void Update() is called repeatedly in Unity
OnDestroy
  When the application stops running (you exit Play mode),
  Turns off LED by writing “0”
  Closes serial port